## Slide 1: Environmental Testing, Design, Analysis for HABs
By: Ara Kourchians (arko)

## Slide 2: About Me
Undergrad at Cal Poly Pomona
  Electrical Engineering – emphasis in control systems
Work for JPL/NASA
  Software engineer for electronic part reliability testing/reporting systems
Previous projects and work
  Omni-directional drive system robots
  Self-balancing robots
  Time machines
  Harsh environment sensors
  Plasma Lighting RF Ballasts
  Many self-funded projects
DISCLAMER
  I am NOT here to represent JPL/NASA, all opinions are my own. Information provided is publically available information (google it yo).

## Slide 3: Assumptions
You already know what a HAB is
Basic understanding of electronics and physics
Goal: Increase the reliability of your HAB

## Slide 4: Failure
Software
Power/Radio Hardware configuration
Environment

## Slide 5: TESTING TESTING TESTING
Software
  Test Harness
  Full flight systems test without debugger, power supply, etc
    “Pretend you are going to launch it”
Power/Radio Hardware configuration
  Know your datasheets
  Full battery test
  Range test & dry run
  EMC
Environment
  Cold, Vacuum, IR, Shake
Input
Code
Output
Verify

## Slide 6: Software Testing
Unit Testing
  Make up data
    neg/pos lat/long
  Test cases
    Bad NMEA packet
    GPS signal loss
  Reset Procedure
  Proper FSM
Integration/System Testing
Static Testing
  Peer review
  Static Code Analysis
  KNOW YOUR EMBEDDED HARDWARE AND COMPILER
Input
GPS
Code
Output
Verify
Input
Radio Code
Output
Verify
Input
System Code
Output
Verify
GPS
Code
Radio Code
System Code
Input
Output
Verify

## Slide 7: Software Standards
What does JPL do? (YES THIS IS PUBLIC INFO)
  People hate following rules and want to follow their own
  Pick 10 standard/rules and make them easy to remember
  Each tied to a real failure
Power of 10 Rules for developing safety-critical code (C language)
  No spaghetti code flow (goto, recursion, etc)
  All loops must have fixed bounds (stops runway code)
  Avoid heap memory allocation (avoid malloc() )
  Keep function line count short (less than ~60 lines)
  At least two runtime assertions per function (verify conditions pre/post func)
  Keep data objects at smallest possible level of scope
  Check functions return value or cast as void, check function input parameters
  Use precompiler for headers and simple macro definitions
  Limit pointer use to a single dereference, no function pointers
  Warnings are errors, must compile with no warnings (set compiler to most pedantic)
Lock down code, any changes means going back and testing all over again
http://web.eecs.umich.edu/~imarkov/10rules.pdf
http://lars-lab.jpl.nasa.gov/JPL_Coding_Standard_C.pdf

## Slide 8
Photographer: Joseph Linaschke

## Slide 9: Power/Radio hardware testing
Know your datasheets, estimate power draw
Good connectors
Power supply test operating voltage range (Vmin to Vmax)
Estimate battery life
Full battery test
Range Test
A good distance
Notes: -Run a power supply test, record current draw and characteristics, estimate battery lifetime
-Full battery test (run it till it dies)
-Get to know your datasheets, assure all parts are operating within expected conditions (not drawing too much or too little current, etc)
-Range Test – Have a buddy drive the payload around in a car, find a distant mountain (or hill if you are in the uk). Using flight hardware and ground radio systems to test.
-EMC Testing – Could be as simple as running all your radios close to each other.
  -Transmit your ham gear near it to test robustness
  -List what an emc test includes, and why most are unnecessary

## Slide 10: EMC & Derating
  Derating (not really necessary for HAB’s)
  Run electronics below maximum rating to increase lifetime/reliability
    Under clock CPU to prevent overheating
    Prevent accidental damage
EMC
  Capacitive, Inductive, Radiative, Conductive
  Could be as simple as running all your radios close to each other
    Power Amplifier degradation
    General interference (especially RX)
  Transmit your ham gear near it to test robustness
    Commercial equipment is usually rated
    Homebrew PCB’s are not rated
http://www.williamson-labs.com/ltoc/glencoe-emc-11.htm

## Slide 11: RUN EMC
Frequency (MHz)
1
10
100
1000
10000
I.E. – Radiated Field Strength (dBuV/m)
10
20
30
40
50
Emission
Susceptibility

## Slide 12: EMC
Radiated (30MHz – 10GHz)
  Emission: Clock & data lines, switching power supplies, poor RF config
  Susceptibility: Clock & data lines in bad places, bad termination
  Solution: Balance transmission lines, ground planes, shielding, correct termination, filters, differential lines
Conducted (100kHz – 30MHz)
  Emission: Switching power supplies, motors, switches, relays
  Susceptibility: Noisy AC power, Poor decoupling on power
  Solution: Decoupling, power filters, shielding, ground planes
http://www.williamson-labs.com/ltoc/glencoe-emc-11.htm

## Slide 13: Environmental Road Map
Understand the environment
Design/Understand your hardware
Determine tests
Build test rig
Test
Analyze
Redesign

## Slide 14: Environment
What are the expected environmental conditions of nearspace?
  Air Temperature: -60C to +40C
  Pressure: 0.01atm (1010Pa) to 1atm (101325Pa)
  Winds: 0mph – 100mph
  Forces: up to 10g
  Humidity: 0% - 100%
  Solar Heat (Irradiance): 180 W/m^2 - 340 W/m^2
  Radiation: <0.1krad/year (to put into perspective: HAB experiences 1 CT scan for each day of flight)

## Slide 15: Environment
Your HAB would need to fly for 10 years at 30km for radiation
to become a legitimate concern
What are the expected environmental conditions of nearspace?
  Air Temperature: -60C to +40C
  Pressure: 0.01atm (1010Pa) to 1atm (101325Pa)
  Winds: 0mph – 100mph
  Forces: up to 10g
  Humidity: 0% - 100%
  Solar Heat (Irradiance): 180 W/m^2 - 340 W/m^2
  Radiation: <0.1krad/year (to put into perspective: HAB experiences 1 CT scan for each day of flight)

## Slide 16: Environment
Solar Flux
IR Sky
Albedo Cloud
Albedo Ground
IR Ground
Convection
Radiation

## Slide 17: Environment
Solar Flux
IR Sky
Albedo Cloud
Albedo Ground
IR Ground
Convection
Radiation
Convection drops off after 18,000m

## Slide 18: Environment
43rd International Conference on Environmental Systems Thermal Design and Analysis of the Supersonic Flight Dynamics Test Vehicle for the Low Density Supersonic Decelerator Project
(doi: 10.2514/6.2013-3348) http://arc.aiaa.org/doi/abs/10.2514/6.2013-3348
Babbage,
2013

## Slide 19: Understand your hardware
Datasheets
  Operating Temperature
  Heat generated (depends on parts)
Your HAB falls in two categories
  Hot HAB – Overheats & fails at altitude
    Power regulator, powerful processor, etc
  Cold HAB - Freezes & fails at altitude
    Low power parts

## Slide 20: What are you testing?
Can your HAB survive the expected temperatures?
  Electronic parts (-40C – +80C)
How well does your insulation work?
Does your HAB overheat? (Do your parts need cooling?)
  Camera
  Power Regulator
  Cutdown
  “New Tech” or “mystery box”
  Anything that acts significantly different in a vacuum

## Slide 21: Spacecraft Thermal Modeling
http://www.esmats.eu/amspapers/pastpapers/pdfs/2012/johnson.pdf
Model & Simulate
  “Everything on” (Hottest Case)
  “Bare minimum” (Coldest Case)

## Slide 22: HAB Thermal Modeling

## Slide 23: How do you know if you’re a hot or cold HAB?
Just test it!
  Room temperature / Ice test
    Cheap ($10)
    Test parts to rating
    Answers questions like:
      does temp increase at room temp?
      How do the characteristics change at cold?
  Build Thermal/Vacuum/IR chamber
    Expensive ($100-200)
    Good test & data

## Slide 24: Environmental Chamber (on a NASA budget)

## Slide 25: Environmental Chamber (on a budget $100-$200)
Air Temperature -60C to +40C: Dry Ice, Hair Dryer
Pressure 0.01atm to 1atm: Refrigerator Pump
Solar heat 184 W/m^2 - 341 W/m^2 : Light Bulb, Heat lamp
Winds/Forces up to 10g: Stairs (Ed Method)
Humidity 0% - 100%: Spray Bottle

## Slide 26: ENV Chamber Design

## Slide 27: ENV Chamber Design - Vacuum
12.7mm polycarbonate
glass
Schedule 40 PVC Tee
Vacuum
Pump
Silicone Rubber

## Slide 28: ENV Chamber Design - Cold
Dry Ice
Peltier
Cooler
Heat Transfer Rod
Heat sink

## Slide 29: ENV Chamber Design – Solar Heat
Light Bulb

## Slide 30: Setup
Sun
Vacuum of nearspace
Deep space or ground
HAB

## Slide 31: Setup
Sun
Vacuum of nearspace
Deep space or ground
HAB
Dry Ice

## Slide 32: Setup – External Cooling

## Slide 33: Poor Results
DEEP SPACE SIDE
SUN SIDE
Cooling Rod
Altitude

## Slide 34: Setup
Sun
Vacuum of nearspace
Deep space or ground
HAB
Dry Ice
Cloth
Fishing Line
Note: Vacuum pump must run continuously

## Slide 35: Setup – Internal Cooling

## Slide 36: Good Results
DEEP SPACE SIDE
SUN SIDE
Chamber Wall Temperature
Altitude

## Slide 37: Results
- Sun Side
- Internal
- Deep Space Side

## Slide 38: Measurements

## Slide 39: Design Improvements
Thermal shroud with Liquid Nitrogen, cold isopropyl, or glycol pumped through the walls
Proper coating for maximum thermal absorptivity
Control System
Lazy Susan

## Slide 40: Now you know…
But how do you solve these thermal problems?

## Slide 41: Solving the thermal problems
Hot HAB
  Radiator – Copper braid & white acrylic paint (high emissivity)
  Aluminum foil or heat blanket (low absorptivity)
  Software (turn things off when not in use, underclock, etc)
Single/Multiple component heating is solved with radiators
  Place radiators on sides or bottom
Deep Space
or
Ground
Earth State
Hot HAB
Radiator
http://ukhas.org.uk/guides:materials
http://www.engineeringtoolbox.com/emissivity-coefficients-d_447.html
http://www.engineeringtoolbox.com/radiation-surface-absorptivitie-d_1805.html

## Slide 42: Solving the thermal problems
Cold HAB
  Insulate - Foamular or Styrofoam (extruded polystyrene)
  Black body - Acrylic craft paint (high absorptivity)
  Heater (wastes power, should have a control system to prevent becoming Warm HAB)
http://ukhas.org.uk/guides:materials
http://www.engineeringtoolbox.com/emissivity-coefficients-d_447.html
http://www.engineeringtoolbox.com/radiation-surface-absorptivitie-d_1805.html
Earth State
Cold HAB
Heater
Insulate

## Slide 43: Solving the thermal problems
MLI (Multi Layer Insulation)
  Aluminum or Silver
  Mylar
  Kapton
  Polyester mesh
  R-value of >>5 K*m^2/W
Foamular
  R-value of 0.88 K*m^2/W
http://ukhas.org.uk/guides:materials

## Slide 44: What is Conformal Coating?
Non conductive dielectric layer for protecting PCB’s
Why Conformal Coating?
Thermal stability and evenness
Conductive heat transfer
Corrosion prevention
Humidity
Accidental shorting
Whiskering
NOTE: Thermal expansion could damage parts
Courtesy of DanielSaul

## Slide 45: Conformal Coating
Acrylic
  Low cost, durable, water resistant, fast dry
Silicone
  Temperature resistant, flexible, water resistant, great insulator
Urethane
  Chemical/Corrosion protection, thermal shock, moisture resistant
Application: Avoid bubbles, don't go too thick or too thin
Recommended Suppliers: MG Chemicals, Techspray
http://www.humiseal.com/product-selector/conformal-coating

## Slide 46: Thanks!
Questions?
Email: arko2600@gmail.com
arkorobotics.com/env